## Slide 1: Posture Alert device
Nikki Metzger, Christian Ralph, and Daniel Lerner

## Slide 2: Project Overview
Wearable posture alert device
  For use while sitting
Three 6 DOF sensors
  Measure body position and angle

## Slide 3
Hunched shoulders
Leaning to the side
Slouching

## Slide 4: Changes
No changes to:
  Need statement/project scope
  Design schedule
  Team responsibilities
Some additions to the design specifications

## Slide 5: Verification Plan
Safety: possibility of injury risk < 1% per use
  Sensor base – heat generation
  Foam tape – skin irritation
  Design safe analysis
Notes: Can I only talk about the most important specs?

## Slide 6: Verification Plan
Accuracy: accurate detection 85% of the time
  Instruct user how to sit (position and angle)
  Must correctly determine the position
Reliability: reliable 85% of the time
  Let user sit ‘naturally’ (not instructed)
  Must consistently detect the position and determine if it’s poor posture

## Slide 7: Verification Plan
Feedback: effective 85% of the time
  Tactile feedback
  Effectively notifies user
Latency: feedback within 3 minutes
  Verify user’s poor posture isn’t temporary movement

## Slide 8: Validation Plan
Who?
  Male and female
  18 - 29 years old
  Minimum of 5 participants

## Slide 9: Validation Plan
How?
  First round:
    Lab-setting clinical tests
    Validate in isolated positions
    85% success rate
      Success: detects and notifies for all poor posture positions

## Slide 10: Validation Plan
How?
  Second round:
    ‘Office’ setting
    Validate for intended use

## Slide 11: Overall Status
Proof of concept testing
  Verify IMU sensors register posture change
  Compare sensor values to goniometer measurements

## Slide 12
Sensors measure yaw, pitch, and roll

## Slide 13: Results of Proof of Concept (Overview)
Sensor at sternum
  roll angle

## Slide 14: Questions?

## Slide 15: Results of Proof of Concept
Posture Position | Hip Angle (deg) | Yaw (deg) | Pitch (deg) | Roll (deg)
Trial 1 |  |  |  | 
Resting | N/A | 15.5 | 8.5 | -67.3
Lean Forward | 6 | 16.4 | 8.6 | -57.3
Return to Rest 1 | 0 | 11.4 | 4.7 | -67.5
Lean Forward | 14 | 16.2 | 8.7 | -48.6
Return to Rest 2 | -5 | 5.7 | 1.4 | -69.7
Trial 2 |  |  |  | 
Resting Position | N/A | 7.3 | 5.1 | -67.4
Lean Forward | 10 | 7.8 | 5.6 | -55.8
Return to Rest 1 | -2 | 6.1 | 3.5 | -65.2
Lean Forward | 11 | 6.8 | 7.2 | -47.7
Return to Rest 2 | -2 | 1.4 | -0.1 | -65.1

## Slide 16: Results of Proof of Concept
Posture Position | Hip Angle (deg) | Yaw (deg) | Pitch (deg) | Roll (deg)
Trial 1 |  |  |  | 
Resting | N/A | 35.4 | -5.2 | 52.5
Lean Forward | 10 | 55.9 | -13.1 | 47
Return to Rest | -2 | 35 | -1 | 55.7
Trial 2 |  |  |  | 
Resting Position | N/A | 40 | 0.11 | 55.44
Lean Forward | 7 | 59.8 | -9.2 | 53.9
Lean Forward | 16 | 86.5 | -18.2 | 48.3
Return to Rest | -1 | 65.71 | 0.34 | 56.8